## Slide 1
MICROSYSTEMS PROJECT
Smart Greenhouse
Monitoring & Control System
Thebe Ledwaba and Precious Skosana | Vaal University of Technology | 2025
ESP32
DHT22
MQTT
React
Mosquitto

## Slide 2
Problem Statement
⚠
Manual Monitoring
Traditional greenhouses require constant human presence to check temperature and humidity inefficient and error-prone.
📉
Crop Loss Risk
Without real-time alerts, environmental changes go undetected, leading to crop damage or total loss.
🔌
No Remote Control
s.
Solution: An automated IoT system that monitors, alerts, and allows remote hardware control in real time.

## Slide 3
System Architecture
DHT22
Sensor
Temp & Humidity
→
ESP32
MCU
WiFi + MQTT
→
Mosquitto
Broker
Local PC
→
React
Dashboard
WebSocket
Hardware Outputs
Green LED
Env Stable
Red LED
Alert State
Buzzer
Audio Alert
LCD Display
I2C 16×2
↑ Bidirectional Control: Dashboard → MQTT → ESP32

## Slide 4
Hardware Components
ESP32 Dev Board
Main microcontroller
Dual-core 240MHz, WiFi 802.11 b/g/n, 38 GPIO pins
DHT22 Sensor
Environmental sensing
Temp: -40 to 80°C (±0.5°C), Humidity: 0–100% RH (±2–5%)
I²C LCD 16×2
Local display
16 columns × 2 rows, I²C address 0x27, backlight enabled
LEDs + Buzzer
Alert outputs
Green GPIO5, Red GPIO2, Buzzer GPIO23 — threshold driven
Push Button
User input
GPIO18, INPUT_PULLUP, toggles LCD between live and average view
Resistors
Current limiting
220Ω on LED lines — protects GPIO pins (max 12mA)

## Slide 5
Software & IoT Stack
ESP32 FIRMWARE
Library
Purpose
DHT.h
Sensor reading
LiquidCrystal_I2C.h
LCD control
PubSubClient.h
MQTT client
ArduinoJson.h
JSON payloads
WiFi.h
Network stack
REACT DASHBOARD
Feature
Detail
Live sensor feed & Remote Monitoring
2s update cycle
Alert banner
Threshold driven
Buzzer toggle
Remote on/off
LED override
Manual control
LCD messaging
16-char remote msg
Threshold editor
Live update to ESP32
Reading history
Last 20 readings

## Slide 6
MQTT Communication Protocol
PUBLISH → greenhouse/data (every 2 seconds)
{ "temperature": 21.4, "humidity": 62, "avg_temp": 21.2, "avg_hum": 63,
"alert": false, "button": 0, "thr_temp": 32.0, "thr_hum": 40.0,
"buzzer_manual": false, "led_manual": false }
SUBSCRIBE ← greenhouse/control (bidirectional commands)
{"command":"buzzer","value":true}
Turn buzzer ON remotely
{"command":"threshold_temp","value":28.0}
Update temp threshold
{"command":"lcd_message","value":"Check water!"}
Send message to LCD
{"command":"led","red":true,"green":false}
Override LED states

## Slide 7
Key Features & Live Demo
01
Real-Time Monitoring
DHT22 reads every 2s. Live temp and humidity streamed over WiFi via MQTT to dashboard.
02
Threshold Alerts
Exceeding thresholds triggers red LED, buzzer, and alert banner on dashboard simultaneously.
03
Remote Hardware Control
Dashboard sends commands to silence buzzer, override LEDs, and update thresholds in real time.
04
LCD Remote Messaging
Type any 16-char message on dashboard — it appears on the physical LCD within milliseconds.
05
Running Averages
ESP32 computes rolling averages over 10 readings. Button toggles LCD between live and average view.
06
Offline Resilience
If WiFi drops, sensor monitoring, alerts, buzzer, and LCD continue operating uninterrupted.

## Slide 8
Conclusion
Successfully built a full IoT monitoring system on ESP32 with real sensor data
MQTT bidirectional communication enables remote hardware control from a web dashboard
System runs offline-resilient — sensor logic continues even if WiFi drops
Architecture is extensible: actuators (pump, fan) and data logging can be layered on
Thank You | Questions Welcome | Thebe Ledwaba and Precious Skosana— VUT 2025